## Slide 1: Repeaters: Borrowing a Tall Tower
How one radio on a hill can stretch your range from 2 miles to 20 or more

## Slide 2: What a repeater does
1
Your radio transmits
On a 467 MHz input channel (shown as 15R–22R)
2
The tower hears you
Its antenna sits high, often 100 feet or more
3
It retransmits instantly
On the matching 462 MHz channel, with more power
4
Everyone in range hears it
Even family members miles beyond your handheld's reach
Why it works
Height is everything in radio. A repeater lends you its height.

## Slide 3: The numbers
5 MHz
gap between what you send and what you hear
8
repeater channels (15R–22R)
20–50
miles of typical coverage
50 W
maximum repeater power
Repeater inputs are for licensed GMRS users only; plain FRS walkie-talkies can't use them.

## Slide 4: Finding and using one
Look it up
Search myGMRS.com or RepeaterBook for towers near you and the ranch
Ask permission
Most repeaters are privately owned; the owner decides who may use them
Set the tone
Repeaters need a specific access tone; the listing gives it
Keep it short
Others share it; pause between messages so someone can break in

## Slide 5: The catch
Great for everyday
Family checks in across the county
Works from inside a car or house
No gear on your roof needed
Don't count on it in a disaster
Many towers lose power when the grid goes down
Some are shut down or full of traffic
Have a direct radio-to-radio plan too

## Slide 6: Remember
Use repeaters for range, but always have a radio-to-radio plan that works without one.