## Slide 1: How GPS Knows Where You Are
Satellites, atomic clocks and a little help from Einstein

## Slide 2: The system by the numbers
31
working satellites, about
12,550
miles up
2
trips around Earth each day
4
satellites needed for a fix
The system is run by the U.S. Space Force and is free for anyone in the world to use.

## Slide 3: How your phone finds itself
1
Each satellite broadcasts the time
From an onboard atomic clock
2
Your receiver notes when each signal arrives
The delay tells how far away the satellite is
3
Three distances pin your position
Like circles that cross at one point
4
A fourth fixes your own clock
Your phone's clock isn't accurate enough alone

## Slide 4: Einstein keeps GPS honest
Two effects on the clocks
Fast-moving clocks run slow (special relativity)
Clocks in weaker gravity run fast (general relativity)
Together, satellite clocks gain about 38 microseconds a day
Why it matters
Light travels about 7 miles in 38 microseconds
Uncorrected, positions would drift about 6 miles a day
Engineers set the satellite clocks slow before launch

## Slide 5: Remember
Every time you use a map app, you're using relativity.