## Slide 1: Why Height Beats Power
The earth curves, and GMRS signals travel in straight lines

## Slide 2: Radio waves travel in straight lines
Line of sight
GMRS works best when the antennas could almost see each other
Hills, buildings and the earth's curve block the signal
Trees and wet leaves soak it up
What that means
Doubling power adds only a little range
Raising the antenna adds a lot
A hilltop beats an extra 5 watts every time

## Slide 3: How far each antenna can 'see'
Antenna height | Radio horizon | Example
6 ft | About 3.5 miles | Handheld at head height
15 ft | About 5.5 miles | Second-story window
30 ft | About 7.7 miles | Mast on the ranch house
100 ft | About 14 miles | Tall tower
200 ft | About 20 miles | Repeater on a high tower
Rule of thumb: radio horizon in miles ≈ 1.41 × √(height in feet). Add both stations' horizons for the most you could hope for over flat ground.

## Slide 4: Putting it together
≈7
miles: two handhelds on flat ground, at best
≈11
miles: handheld to a 30 ft ranch mast
≈23
miles: handheld to a 200 ft repeater
1–2
miles: real life in hills and trees
These are best-case figures over flat, open land. Arkansas hills and forest cut them down sharply.

## Slide 5: Remember
Before buying more power, get the antenna higher.