## Slide 1: Antennas 101
The cheapest way to double what your radio can do

## Slide 2: Four kinds of GMRS antennas
Type | Where it goes | What it does
Stock "rubber duck" | On the handheld | Short and tough, but the weakest
Long whip (15–18 in) | On the handheld | Noticeably better range, still portable
Magnet-mount | Truck roof | Uses the metal roof as a ground plane; big gain over a handheld inside a cab
Base antenna (J-pole or similar) | Mast or roofline | Highest and best; the backbone at the ranch

## Slide 3: Getting it right
Match the connector
UV-5G Plus takes SMA-female antennas; check before ordering
Mount it high
Every foot of height helps more than extra watts
Keep cable short
Long, thin coax wastes signal; use quality low-loss cable
Never transmit without it
Talking with no antenna attached can damage the radio
Source: True Prepper: Best GMRS radios

## Slide 4: Inside a vehicle
Handheld in the cab
Metal body blocks much of the signal
Range can drop by half or more
Hold it near a window at least
Roof antenna outside
Signal goes out in every direction
Pair with a mobile radio up to 50 W
Best upgrade for the drive to the ranch

## Slide 5: Remember
A $25 antenna placed high often beats a $200 radio placed low.