## Slide 1: Which Radio Is Which?
FRS, GMRS, CB, MURS and ham radio side by side

## Slide 2: Five radio services compared
Service | License | Max power | Good for
FRS | None | 2 W | Store-bought walkie-talkies, kids, short range
GMRS | $35, no test, family | 50 W | Family plans, farms, repeaters
CB | None | 4 W (AM) | Truckers, older farm radios
MURS | None | 2 W (VHF) | Ranch and business use, 5 channels
Ham | $35 + exam | Up to 1,500 W | Long distance, emergency networks
Sources: Midland: FRS, GMRS, CB, ham differences; FCC

## Slide 3: Why GMRS fits a family
One license
Covers spouse, children and more
No exam
Anyone in the family can use it today
Talks to FRS
Neighbors' cheap walkie-talkies share channels 1–22
Repeaters and power
Up to 50 W and access to towers

## Slide 4: When to add another
Add ham radio if you want
Statewide or worldwide reach
Connection to emergency nets
More bands and more learning
Keep a CB if you want
To hear truckers on the highway
Road and traffic news during evacuations
Channel 19 is the trucker channel

## Slide 5: Remember
GMRS for the family, ham for the long haul, CB for the highway.