## Slide 1: Your Neighbors Already Have Radios
GMRS can talk to the cheap walkie-talkies in most closets

## Slide 2: Shared channels
22
channels shared by FRS and GMRS
2 W
FRS max on channels 1–7 and 15–22
0.5 W
everyone's max on channels 8–14
0
licenses needed for FRS
Your UV-5G Plus on channel 3 can talk to a $30 blister-pack walkie-talkie on channel 3.

## Slide 3: Why that matters
Neighborhood help
Check on elderly neighbors during an ice storm
Kids and grandkids
Hand them a simple FRS radio; no license or setup
Visitors at the ranch
Guests can join with whatever radio they bring
Listening in
Hear what's happening nearby during an outage

## Slide 4: Make it work
1
Match the channel number
FRS channel 3 = GMRS channel 3
2
Turn privacy codes off
Or match them exactly on both radios
3
Stay on 1–22
FRS radios can't reach repeater channels
4
Expect shorter range
FRS radios are lower power with fixed antennas

## Slide 5: Remember
Keep two or three cheap FRS radios in the go bag to hand out.