## Slide 1: Making Batteries Last a Week
In a long outage, battery life matters more than range

## Slide 2: Where the battery goes
Transmitting
Uses the most power by far
High power drains it fastest
Short messages save a lot
Listening
Uses far less
But it adds up when left on all day
The screen light uses some too

## Slide 3: Stretch every charge
Listen on a schedule
First 10 minutes of each hour instead of all day
Use Low power up close
Save High for long distance
Talk less
Plan what to say before pressing the button
Dim the screen
Shorten the backlight time in the menu

## Slide 4: Ways to recharge
Source | How | Notes
Wall outlet | USB-C cable | Top off whenever there's power
Power station | USB port | One 1,000 Wh unit can charge a radio dozens of times
Vehicle | USB car adapter | Charge while driving to the ranch
Solar | Small USB panel | Slow but endless
Spare battery | Swap in | Keep one charged in the go bag

## Slide 5: Remember
Two charged batteries and a schedule beat one battery left on all day.