## Slide 1: Radios for the Truck and the Ranch
Mobile and base stations reach far beyond any handheld

## Slide 2: Handheld vs mobile vs base
Type | Power | Antenna | Best place
Handheld | Up to 5 W | Short, on the radio | Pocket and go bag
Mobile | Up to 50 W | Roof of the vehicle | Truck and family cars
Base | Up to 50 W | High mast or roof | Ranch house and home
Source: FCC GMRS rules, 47 CFR Part 95

## Slide 3: A base at the ranch
Mast antenna
30 feet or higher, clear of trees
Runs on solar
A mobile radio draws little; your Victron system can power it
Always listening
Someone at the ranch can hear arriving family
Guides the drive in
Reach the truck several miles out

## Slide 4: Setting up the truck
1
Mount a mobile radio
Under the dash or seat, with the control head in reach
2
Magnet-mount antenna on the roof
Centered for the best pattern
3
Wire to the battery with a fuse
Not a cigarette-lighter plug for 50 W
4
Program the family channels
Same plan as the handhelds

## Slide 5: Remember
One good base at the ranch turns every handheld into a long-range radio.