## Slide 1
Meet the Yaesu FT-65R
A tough, simple dual-band handheld for the family

## Slide 2
The controls
Push-to-talk (PTT)
Side button; hold to talk, release to listen
Dial
Changes frequency or memory channel
V/M key
Switches between VFO and memory mode
MONI
Opens the squelch so you can hear weak signals
Ham Family Series · 4 of 15
2

## Slide 3
VFO or memory?
VFO mode
Dial any frequency directly
Good for exploring and testing
Easy to land on the wrong spot
Memory mode
Saved channels with offsets and tones
Best for family use
Program them once with CHIRP
Ham Family Series · 4 of 15
3

## Slide 4
Worth buying with it
Accessory | Why
Longer whip antenna | Noticeably better range than the stock antenna
Spare battery | A full day of standby and talk without charging
SCU-35 programming cable | Load channels from the laptop with CHIRP
Car charger or USB cable | Charge in the truck on the drive to the ranch
Check the battery and charger part numbers against the FT-65R before you buy.
Sources: Yaesu FT-65R operating manual
Ham Family Series · 4 of 15
4

## Slide 5
Remember
Program the family channels into memory, keep the power on high for distance, and carry a spare battery.