## Slide 1
Repeaters: Offsets and Tones
How a mountaintop radio turns your 5 watts into 50 miles

## Slide 2
How a repeater works
1
You transmit on its input
Usually 600 kHz away from the output on 2 meters
2
It checks your tone
The right CTCSS tone opens the repeater
3
It retransmits on its output
From a tall tower with more power
4
Everyone in range hears you
Across a whole county or more
Offsets
2 meters: 600 kHz, plus or minus. 70 centimeters: 5 MHz, usually plus.
Ham Family Series · 5 of 15
2

## Slide 3
Repeaters to program first
Repeater | Output | Offset | Tone
W4CAT Nashville | 146.955 | + | 114.8
K5PXP Mount Nebo (ranch) | 146.820 | – | 131.8
N4OEM Nashville ARES | 442.750 | + | 100.0
N5XMZ Magazine Mountain | 443.250 | + | 114.8
Listings change. Check RepeaterBook before you rely on one, and listen first.
Ham Family Series · 5 of 15
3

## Slide 4
Good repeater manners
Listen first
Make sure no one is using it
Pause between turns
Leave room for someone with an emergency
Say your call sign
'W4JUM monitoring' is all it takes
Keep it short
Many repeaters time out after a few minutes
Sources: RepeaterBook listings; ARRL repeater guidance
Ham Family Series · 5 of 15
4

## Slide 5
Remember
Right frequency, right offset, right tone; then listen before you talk.