## Slide 1
Simplex: Radio to Radio
When the repeater is down, talk straight to each other

## Slide 2
Key simplex frequencies
146.520
2 m national calling
446.000
70 cm national calling
1–3
miles, handheld to handheld
0
towers needed
Call on the calling frequency, then move to another simplex channel to keep talking.
Ham Family Series · 6 of 15
2

## Slide 3
A family simplex plan
1
Pick a main channel
For example 146.550
2
Pick a backup
For example 146.580, in case the main is busy
3
Save both in memory
Name them FAM1 and FAM2
4
Practice monthly
Test from home, the truck and the ranch
Why it matters
Repeaters can lose power in a storm. Simplex works as long as your batteries do.
Ham Family Series · 6 of 15
3

## Slide 4
How far simplex reaches
Setup | Typical range
Handheld to handheld, in town | 1 to 3 miles
Handheld from a hilltop | 5 to 15 miles
Truck radio to truck radio | 10 to 20 miles
Base antenna to base antenna | 20 to 40 miles
Estimates for open terrain; hills and trees cut range sharply.
Sources: ARRL band plan; typical VHF line-of-sight estimates
Ham Family Series · 6 of 15
4

## Slide 5
Remember
Every family plan needs a simplex channel that works with no tower at all.