## Slide 1
Programming with CHIRP
Load every family channel in minutes, the same way on every radio

## Slide 2
Program the FT-65R
1
Install CHIRP
Free from chirpmyradio.com
2
Connect the SCU-35 cable
Radio off, cable in, then radio on
3
Download from radio
Radio menu, choose Yaesu FT-65
4
Edit the channels
Frequency, offset, tone and a short name
5
Upload to radio
Save the file first as a backup
Tip
Always download first, then save the file before you change anything.
Ham Family Series · 7 of 15
2

## Slide 3
One row in CHIRP
Field | Example
Frequency | 146.955000
Name | W4CAT
Duplex / Offset | + / 0.600000
Tone mode / Tone | Tone / 114.8
Keep names short, 6 to 8 letters, so they fit on the screen.
Ham Family Series · 7 of 15
3

## Slide 4
Make it a family system
Same list everywhere
Channel 1 means the same thing on every radio
Number by purpose
1–5 family, 6–20 repeaters, 21+ weather
Import repeaters
CHIRP can pull nearby listings from RepeaterBook
Print a card
Tape a channel list inside the radio case
Sources: CHIRP project documentation
Ham Family Series · 7 of 15
4

## Slide 5
Remember
Download, save, edit, upload, and give every family radio the same channel list.