## Slide 1
Power When the Grid Is Down
A radio is only as good as its battery

## Slide 2
Power options
Source | Runs | Notes
Radio battery | About a day | Carry a charged spare
AA battery case | Hours to a day | Use lithium AAs in cold
Truck 12 V outlet | As long as you have fuel | Don't drain the starting battery
Solar and a battery bank | Days to weeks | The ranch system can run a base station
Receiving uses little power; transmitting on high uses the most.
Ham Family Series · 12 of 15
2

## Slide 3
Stretch your battery
Use low power
Switch to high only when needed
Listen on a schedule
Check in at set times instead of all day
Keep it warm
Cold batteries lose capacity
Rotate spares
Charge and test them every month
Ham Family Series · 12 of 15
3

## Slide 4
At the ranch
What you have
Solar panels and a LiFePO4 battery bank
A 12-volt or 24-volt system
Space for a base antenna
What to add
A 12 V DC supply or converter for the radio
A fused power lead
A mast antenna on the shed
Sources: ARRL emergency power guidance; general battery practice
Ham Family Series · 12 of 15
4

## Slide 5
Remember
Carry spares, transmit on low, listen on a schedule, and let the sun recharge the rest.